## Slide 1
David Rach, Ph.D.
UMGCCC Flow Cytometry Shared Resource
Baltimore, MD
October 23, 2026
Slides
Towards ‘No Cell Left Behind’: open-source tool sets to
leverage Spectral Flow Cytometry’s full biological discovery potential

## Slide 2: Spectral Flow Cytometry is amazing!!!
Capable of resolving remarkably similar fluorophores → increased number of markers per panel compared to conventional flow cytometry (CFC)
Allows for rapid acquisition of millions of events in a few minutes → typically greater number of acquired cells per sample compared to mass cytometry (MC)
Spectral Flow Cytometry (SFC) datasets have an unique combination of width and depth compared to preceding technologies

## Slide 3: Spectral Flow Cytometry is amazing!!!
Expand our knowledge about immune system heterogeneity
Able to efficiently acquire greater number of cells → more thorough profiling of rare cell subsets
Build one panel, evaluate multiple cell types → invaluable for studies with limited biospecimen

## Slide 4: Trade-off: Increasing analytical complexity
If you are only interested in a single population of cells → analysis process remains essentially unchanged (manual gating with a few more gates)
If your goal is to characterize all cell populations that may be present →
the breadth and depth of the datasets complicate the analysis

## Slide 5: Complex Datasets: Combinatorially Exponential Clusters
And at the end, we grouped cells that only expressed the same markers
“Groups” per panel = 2Number of Fluorophores
If for a given marker in your panel, you split the cells into positive and negative populations
And this splitting process was repeated for every marker in your panel

## Slide 6: Complex Datasets: Combinatorially Exponential Clusters
And at the end, we grouped cells that only expressed the same markers
9-color CFC panel → 512 groups at most
40-color SFC panel → 1.1e+12 groups (trillion)
If for a given marker in your panel, you split the cells into positive and negative populations
And this splitting process was repeated for every marker in your panel
60-color SFC panel → 1.2e+18 groups (quintillion)

## Slide 7: What even is a quintillion?
1 gate, every 10 seconds → 6 groups/minute
60-color SFC panel → 1.2e+18 groups (quintillion)
60 minutes in an hour → 360 groups/hour
Awake 16 hours a day → 5760 groups/day
365 days per year → 2,102,400 groups/year
If I were to manually check for every combination...

## Slide 8: What even is a quintillion?
1 gate, every 10 seconds → 6 groups/minute
60-color SFC panel → 1.2e+18 groups (quintillion)
60 minutes in an hour → 360 groups/hour
Awake 16 hours a day → 5760 groups/day
365 days per year → 2,102,400 groups/year
If I were to manually check for every combination...
….Not even close….

## Slide 9
60-color SFC panel → 1.2e+18 groups (quintillion)
365 days per year → 2,102,400 groups/year
Invent a time-machine, become immortal
13.8 billion years → 2.9e+16 groups/reality
Continuously since the Big Bang

## Slide 10
60-color SFC panel → 1.2e+18 groups (quintillion)
365 days per year → 2,102,400 groups/year
Invent a time-machine, become immortal
13.8 billion years → 2.9e+16 groups/reality
Continuously since the Big Bang
….Still not enough….

## Slide 11
60-color SFC panel → 1.2e+18 groups (quintillion)
365 days per year → 2,102,400 groups/year
So we need ~ 50 immortal researchers working continuously since the Big Bang just to check all group combinations for a single 60-fluorophore panel .fcs file
Invent a time-machine, become immortal
13.8 billion years → 2.9e+16 groups/reality
Continuously since the Big Bang

## Slide 12
60-color SFC panel → 1.2e+18 groups (quintillion)
365 days per year → 2,102,400 groups/year
So we need ~ 50 immortal researchers working continuously since the Big Bang just to check all group combinations for a single 60-fluorophore panel .fcs file
Invent a time-machine, become immortal
13.8 billion years → 2.9e+16 groups/reality
Continuously since the Big Bang
1 file down, 99 more to go!

## Slide 13: Alternative: Unsupervised Analysis (Algorithms)
Consequently, if the goal is to characterize all cell populations present, some form of unsupervised (algorithm) or semi-supervised analytical approaches will be needed
Consequently, if the goal is to characterize all cell populations present, some form of unsupervised (algorithm) or semi-supervised analytical approaches will be needed
Clustering → FlowSOM, Phenograph, Xshift, etc.
Dimensionality visualization → opt-SNE, UMAP, PaCMAP, Phate, etc.
Automated Gating → openCyto, flowMagic, ElasticGate, etc.

## Slide 14: The challenge for unsupervised approaches

## Slide 15: The challenge for unsupervised approaches

## Slide 16: The challenge for unsupervised approaches

## Slide 17: The challenge for unsupervised approaches

## Slide 18
Many of these software tools were originally implemented as R or Python packages, for use in analysis of mass cytometry or single-cell RNA-seq datasets
Mass cytometry → similar number of markers, typically fewer events, no unmixing variation due to autofluorescence
Adapted algorithmic tools struggle with number of events
Single-cell RNA-seq → substantially more markers, typically way fewer events. No equivalent “negative” gate events for not expressed transcripts
Down-sampling becomes often necessary

## Slide 19
Adapted algorithmic tools struggle with unmixing errors
Adapted software packages heavily rely on having a consistent median fluorescent intensity (MFI) to cluster cells based on positive or negative marker expression
Unmixing errors can seriously shift the MFI ranges for “negative” and “positive” cells for individual acquired specimens
Existing batch correction / normalization / scaling tools target instrumental or experimental level variation for correction

## Slide 20
“We discovered a novel dendritic cell cluster”
Despite the critical importance unmixing controls play, few tools permit us to determine quality of the individual control before unmixing
Existing quality control algorithms (PeacoQC, FlowAI, etc.) primarily focus on detecting laser and fluidic issues in already acquired .fcs files.
Unmixing errors can be introduced by tandem degradational, additional autofluorescences, undiagnosed instrumental issues, etc.

## Slide 21
Full biological discovery potential often out of reach
For most spectral flow cytometry datasets, only a handful of cell populations end up being analyzed by any method
Most flow cytometrist don’t code
You likely lost your bioinformatician while describing manual gating
The statisticians were never consulted

## Slide 22: Personal Goal: No cell left behind
Repeated 3 AM thoughts
What makes spectral flow cytometry data amazing is both the depth and the breadth
How to fully profile the entirety of the acquired dataset, not just a single cell population of interest

## Slide 23: My PhD’s focus: HIV-exposed Uninfected Infants

## Slide 24: Our Malawian Cohort

## Slide 25: Study Timeline

## Slide 26: 32-Fluorophore Spectral Flow Cytometry Panel

## Slide 27
To unlock the comprehensive biological discovery potential,
we need to address these pink elephants
Quality of the unmixed full-stained data is linked to the quality of our single-color controls (and our ability to provide appropriate autofluorescence controls).
If we are acquiring 3 million cells to detect 100 rare cells, how do we thoroughly explore the rest of the sample to avoid wasting useful data?

## Slide 28
Building open-source tool-sets to address SFC’s quirks
Spectral Signature Characterization and Isolation
Automated Instrument
Quality-Control Dashboards
Incorporation of manually-annotated gating information
Rust

## Slide 29: Previously looked at unconventional T cells
Shifting from 50%-50% FlowJo – R to increasingly more R
Paper
Building around reproducibility from the start (not as an after thought)
Improved Bioconductor interoperability
Main differences this time around:
Targeted re-writes in Rust to speed up original R code

## Slide 30: Semi-supervised Pipeline

## Slide 31: Pipeline: Acquisition
Acquired day of staining on a 5-Laser Cytek Aurora
Instrument flushed with 10% Contrad and Water for 20 minutes pre-use
Instrument passed by both the UMGCCC FCSR and Cytek’s QC criteria immediately before acquisition
UMGCCC FCSR
InstrumentQC
Dashboard
Plots for our
5L Aurora
Dashboard
How-To-Set-Up
Historical Data
5L Aurora

## Slide 32: Automated Daily Processing
Behind-the-scenes:
Using R (and increasingly Rust) to process the .fcs files
Our Quarto Website gets updated twice daily via a GitHub action
Automated transfer to GitHub via Windows Task Scheduler

## Slide 33: Instrument Quality Control Dashboard
Dashboard
How-To

## Slide 34: Instrument Quality Control Dashboard

## Slide 35: Pipeline: Evaluating Unmixing Controls
Luciernaga
Luciernaga
Vignette
New unmixing controls acquired with each experiment.
Extra specimen cells acquired as additional unstained controls
Unmixing Controls are screened for suitability for unmixing
Single-colors: Tandem degradation, and autofluorescence contamination
Unstained(s): Presence of multiple-autofluorescences in lymphocyte gate
Flagged unmixing controls are replaced with equivalents from adjacent experimental date

## Slide 36: Luciernaga: Individual Cell Normalized Signatures
Code

## Slide 37: Automated tools for screening unmixing controls
Autofluorescence Isolation
Residual Autofluorescence
APC-Fire 810
APC
Tandem Degradation

## Slide 38
When the fluorophore degrades, noticeable increase in variant signatures, making up substantial proportion of all cells in the unmixing control
Automated screening all acquired unmixing controls from campus users during off-hours
Identifying degrading fluorophores
Fluorophores in good shape → one predominant normalized signature within the unmixing control raw .fcs file

## Slide 39
This approach also works to isolate variant autofluorescence signatures from unstained controls
Return directly as an .fcs file containing just cells with same signature for use as an autofluorescent tag in SpectroFlo
Unlike other approaches, the isolated cells share normalized signatures, only differing in terms of brightness
Isolating additional autofluorescence signatures

## Slide 40
“As bright or brighter”
Identifying and switching these dim cell single-color controls to bead single-color controls significantly improved unmixing for our panels
Dim antigen-fluorophore combinations acquired as cell single-color controls often have residual autofluorescence contribution to their signature
Residual autofluorescence in dim cell single-color controls
Signature with
residual AF
Signature without
residual AF

## Slide 41: Pipeline: Unmixing
TRU-OLS
TRU-OLS
Walkthrough
AutoSpectral
AutoSpectral
Walk-through
Unmixing Method Agnostic
Unmixing in SpectroFlo (with modified single-color and unstained inputs via Luciernaga)
Unmixing in R
- OLS (Luciernaga using Rust)
- TRU-OLS (via Julia wrapper)
- AutoSpectral

## Slide 42: Pipeline: File Checks
PeacoQC
PeacoQC Vignette
FlowAI
FlowAI
Vignette
PeacoQC in Rust
Checking for fluidic or laser-related issues in the unmixed files
R: PeacoQC or FlowAI
Rust: PeacoQC (thanks James!)

## Slide 43: Pipeline: Manual and Automated Gating
flowGate
flowGate
Walkthrough
openCyto
openCyto
Walk-through
flowMagic
flowMagic Manual
Doublets, Debris, Dead cell cleanup (in R or FlowJo)
Automated Gating for major cell subsets (openCyto or flowMagic)
All automated gate placements visualized via export to a .pdf

## Slide 44: Pipeline: Save to FlowJo v10 .wsp
flowWorkspace
CytoML
FlowJo to R
R to FlowJo
Data for Statistics
Walkthrough
Everything is saved to a FlowJo v10 .wsp, via CytoML
Any automated gates that need adjustment get corrected
Major cell subset statistics exported and analyzed

## Slide 45: Pipeline: Iterating through cell subsets
GatingSets
Walkthrough
Coereba
Vignette
Subset Export
Walkthrough
Coereba
Cell subset of interest exported out as own .fcs
All cell subset .fcs files brought into R

## Slide 46: Pipeline: Coereba
GatingSets
Walkthrough
Coereba
Vignette
Subset Export
Walkthrough
Coereba
Coereba

## Slide 47: Coereba
Code

## Slide 48: Grouping cells that share every marker

## Slide 49: Initial automated gate, with ability to adjust
Initial gates for designated markers calculated via openCyto (mindensity)
Ability to update gate_range constraints
Launch a Shiny app and designate interactively

## Slide 50: CoerebaID column gets added to the .fcs file

## Slide 51: Pipeline: Summarized Experiment
Data stored in a Summarized Experiment
Interoperability with Bioconductor statistics packages

## Slide 52: Summarized Experiment
Permits rapid re-aggregation of the terminal nodes for re-evaluation
Ties in with downstream Bioconductor statistics packages
Portable. Don’t like how we aggregated groups of cells? File is small enough to store in the same data repository as .fcs files for subsequent re-analysis.
Filterable by metadata or node.
- Nodes only in HEU-hi?
- Nodes unique to one individual?

## Slide 53: Retrieval of marker expressions

## Slide 54: Pipeline: Normalization
CytoNorm
Vignettes
CyCombine
Vignettes
CytoNorm
CyCombine

## Slide 55: Pipeline: Clustering
FlowSOM
Vignettes
FlowSOM

## Slide 56: Pipeline: Dimensionality Visualization
UMAP
Wrapper
UMAP
PaCMAP
Wrapper
PaCMAP

## Slide 57: Ability to contrast unsupervised methods vs. “manual” ground-truth

## Slide 58: Retrieving and re-enumerating
1) Gate
3) Re-enumerate
and plot
2) Retrieve manual-annotated gates

## Slide 59: Retrieve manual annotated gating information following unsupervised steps

## Slide 60: Functional and Iterative: plenty for everyone to dislike 
Fun off-label uses thus far:
Contrasting where “manually-gated” cells end up vs. our unsupervised methods (normalization, clustering, etc.)
Added benefit of looking-at-the-forest: Easy to identify badly cryopreserved specimens where cell populations were lost

## Slide 61: Are our high-dimensional analysis problems fixed?

## Slide 62: Semi-supervised Pipeline

## Slide 63: What good is any tool if the community is not able to use it?
Few resources to learn Cytometry in R to begin with
Those that exist aimed at those with intermediate-advanced R skills, not beginners
Know-how concentrated at a few institutions
Most self-learning attempts end in frustration

## Slide 64: Cytometry in R: A free weekly course for flow cytometrist with no-to-little coding experience
Website

## Slide 65: Half-way through this passion project
Wrapping up Cytometry Core module
Gathering steam to start on the Unsupervised Analysis section

## Slide 66: Acknowledgments
Dr. Cristiana Cairo
Dr. Kirsten E. Lyke
Dr. Xiaoxuan Fan
All mothers and their infants, and their communities
All the open-source contributors, developers, and maintainers, that collectively made the tool sets without which all of this would not be feasible
Cytometry
Discord
Bioconductor
Zulip
Dr. Daniela Franco
Dr. Natarajan Ayithan
U01 HD092309
This publication was supported by funds through Maryland Department of Health’s Cigarette Restitution Fund Program – CH- 649-CRF and the National Cancer Institute – Cancer Center Support Grant (CCSG) – P30CA134274.d Service
www.linkedin.com/in/david-rach/
Want to collaborate? Reach out!

## Slide 67: Questions?
UMGCCC FCSR
InstrumentQC dashboard
YouTube @CytometryInR
Website - CytometryInR
Luciernaga
Coereba
InstrumentQC How-To